## Slide 1: Testing Photomultiplier Tubes for nEXO’s Outer Detector
2024 CASST Competition
Lazar Paroski
Queen’s University
August 19 2024
Notes: :)
Just say title

## Slide 2: Outline
Introduction to 0vββ and nEXO
Designing the PMT testing Setup Cooling Loop
  Intro to the PMT Testing Setup
  Initial Design Ideas
  Calculations
  Bill of Materials and Concerns
  Improved Design
  Calculations
  Final Bill of Materials
Future Setup
  Design
  Calculations
  Bill of Materials
Data Analysis Script Improvements
  Data Management Improvements
  FFT and Peak Isolation Stress Test
Conclusion
Notes: :)
Intro to 0vbb and nEXO
Cooling loop
Data

## Slide 3: 2vββ vs 0vββ
2vββ
Qββ
2vββ spectrum measured in 136Xe with EXO-200!
Adapted from: https://arxiv.org/pdf/1108.4193
0vββ signature is peak at nucleus Q value
Peak Smeared by energy resolution?
Introduction to 0vββ and nEXO
Notes: :)
antiv majorana (own antiparticle)
Should see at nucleus Q value
Haven’t seen it yet

## Slide 4: nEXO Experiment
5-tonne single-phase liquid Xenon Time Projection Chamber (TPC)
Enriched to 90% in isotope 136Xe
OD used for passive and active shielding
Target half-life sensitivity of 1.35 · 1028 years
Source: https://nexo.llnl.gov/nexo-overview
Introduction to 0vββ and nEXO
Notes: :)
5t tpc
Enriched in 90% isotope…
Outer detector muon veto
Target half life 10^28

## Slide 5: nEXO Outer Detector (OD)
[1] Search for double-beta decay of 136Xe to excited states of 136Ba with the KamLAND-Zen experiment https://arxiv.org/pdf/1509.03724
Source: https://escholarship.mcgill.ca/concern/theses/j9602648j
Introduction to 0vββ and nEXO
Passive and active shielding
Q value for 0vββ 136Xe → 136Ba is 2458 keV [1]
Muons passing through TPC can create neutrons that can create energy signatures around Q value :(
OD is veto for TPC by detecting Cherenkov radiation :)
Notes: :)
125 PMTs
Passive and active
Underground and muons can knock neutrons that can create false signals
Detecting muons helps us ignore those signals

## Slide 6: The PMT Testing Setup
Located at Laurentian University
PMT attached to barrel lid
Barrel lid in dark enclosure
This will help learn for future setups
Intro to the PMT Testing Setup
Notes: :)
Go over setup

## Slide 7: The PMT Testing Setup
Barrel needs a way to change and keep stable temperature
OD will be held at 12°C
PolyScience AP15R-40-A11B refrigerated circulator
Intro to the PMT Testing Setup
Notes: :)
Barrel closed
Need coller to stabilize temperature

## Slide 8: Design Ideas
Coil Inside Barrel
Coil Outside Barrel
Each setup has some pros/cons
I updated CAD models in Fusion 360
Initial Design Ideas
Notes: :)
2 Ideas
Drawbacks

## Slide 9: Calculations — Simple
Time to cool barrel from 25 °C to 10 °C,
P = 956 W (Cooling Capacity at 17.5 °C )
Time with no heat leaking in barrel :
Time with Insulation with an R-Value of 2:
t = 4.07 Hours
t = 4.14 Hours
Calculations
Notes: :)

## Slide 10: Calculations — Coil in Barrel
dQ/dt < 956 W – Area of coil is bottleneck cooling
dQ/dt = 956 W – Coil exchanges heat at the same rate as the cooler:
dQ/dt > 956 W – Making coil longer has no cooling benefits
L = 4m
Will Cool in 4.14 Hours if more than 4m of tubing is used
Calculations
Notes: :)

## Slide 11: Calculations — Coil Outside of Barrel
Too Long to cool
Don't want to use more than 15m of coil
Calculations
Notes: :)

## Slide 12: Bill of Materials
Still concerns with setup
Coil in barrel could interfere with detection
Setup has additional Issues…
Bill of Materials and Concerns
Notes: :)

## Slide 13: Quick Connect Concerns
Cooler max Pressure: 4.35 Psi
Cooler max Flow Rate: 20.1 lpm
Bill of Materials and Concerns
Notes: :)

## Slide 14: Improved Design
TRACIT-1100 heat transfer compound
Heat transfer coefficient: 114-227 W/m²*K
Relatively inexpensive solution
Avoids quick connect flow and spillage issues
Avoids coil interfering with detection issues
Improved Design
Notes: :)

## Slide 15: Calculations
Used thermal resistance
Putty buffer is amount of putty on either side of tubing
Cooling time reasonable making this option feasible
Calculations
Notes: :)

## Slide 16: Final Bill of Materials
Avoids issues with previous set up by putting coil outside of barrel
BOM was ordered
Final Bill of Materials
Notes: :)

## Slide 17: Design
Same as successful barrel design
Heat transfer putty will be used, and coil is outside pressure vessel
I made CAD model for PV from scratch in Fusion 360
Future Setup
Notes: :)

## Slide 18: Calculations
Fast cooling time
Can use less coil for PV due to this
This is good for space reasons since PV is smaller than barrel
Future Setup
Notes: :)

## Slide 19: Bill of Materials
Very affordable BOM
Can reuse parts from barrel setup
Future Setup
Notes: :)
Transition to next part
  Mention in passing the data improvements

## Slide 20: How the Code Works
The oscilloscope captures chunks of PMT data
FFT is applied to convert the data to the frequency domain for filtering
Inverse FFT brings it back to time domain
Peak detection marks the start and end of peaks based on set amplitude thresholds
I made a script that lets me analyze what is happening visually
FFT and Peak Isolation Stress Test
Notes: :)

## Slide 21: Issue Found through Testing
Code is marking peaks that are too small as signals
Easy fix!
Can adjust thresholds for peak detection to >-0.0005 V (peaks are negative)
Can verify if it works with visualization code I made
FFT and Peak Isolation Stress Test
Notes: :)

## Slide 22: Improvement Results
FFT and Peak Isolation Stress Test
Quick fix, but important issue to discover
Would have had incorrect dark rate
Notes: :)

## Slide 23: Conclusion
Conclusion
Designed multiple potential cooling systems
Made CAD models for the various setups
Did calculations to identify the best approach
Made bills of materials for multiple designs and ordered parts for the final design
Did the above for the future testing setup (Pressure Vessel)
Made improvements to how data is managed for data analysis
Stress tested FFT and peak isolation scripts and made improvements
Notes: :)

## Slide 24: Acknowledgements
Thank you to:
Dr. Erica Caden
Anita Masuskapoe
Dr. Ubi Wichoski
SNOLAB and the nEXO collaboration for making this great summer possible!
Conclusion
Notes: :)

## Slide 25: Backups

## Slide 26: Double Beta Decay – 2vββ
Source: https://arxiv.org/pdf/1109.5515
2vββ decay is rare
Candidate isotopes: even-even nuclei where single β decay is forbidden
Observed in 14 isotopes
Introduction to 0vββ and nEXO
Notes: :)
n → p e antiv twice
Happens with …
Rare
nEXO uses…

## Slide 27: Isotopes that can Undergo 2vββ

## Slide 28: Linear Interpolation for Cooling Capacity
Most Calculations Look at cooling time from 25 °C to 10 °C
Middle is 17.5 °C
Cooling Capacity at 20 °C is 1000 W and at 0 °C is 650 W
Average Cooling Capacity is:
956 W

## Slide 29: Calculations - Simple
Simple Calculation with R-Value 2 Insulation:
Simple Calculation Perfect Insulation:
Coolers Max Cooling Capacity is 956 W
Time to cool from 25 °C to 10 °C

## Slide 30: Calculations — Coil in Barrel
Cooling Capacity depends only on A. This gives 3 cases for dQ/dt that only depend on A:
dQ/dt < 956 W – Area of coil is bottleneck cooling
dQ/dt = 956 W – Coil exchanges heat at the same rate as the cooler
dQ/dt > 956 W – Making coil longer has no cooling benefits
Increasing coil length past 4m has no benefits

## Slide 31: Calculations — Coil Outside of Barrel

## Slide 32: Quick Connect Concerns

## Slide 33: Calculations Outside Barrel Final

## Slide 34: Calculations PV

## Slide 35: Time for Exterior to Heat Barrel by 1 °C wrt R-Value

## Slide 36: Data Management Improvements
PMT_Data_Folder
├── Other Folders and files (not relevant)
└── Data
├── 1
│ ├── Other files (not relevant)
│ └── pmt-1560_noise_closed_loff-2023-11-23
│ ├── C2pmt-1560-noise-000000
│ ├── C2pmt-1560-noise-000001
│ ├── C2pmt-1560-noise-000002
│ └── ...
├── 2
│ ├── Other files (not relevant)
│ └── pmt-1560_noise_closed_loff-2023-12-4
│ ├── C2pmt-1560-noise-000000
│ ├── C2pmt-1560-noise-000001
│ ├── C2pmt-1560-noise-000002
│ └── ...
└── ...
Having to hard code file and folder names every time you change something.

## Slide 37: Data Management Improvements
PMT_Data_Folder
├── Other Folders and files (not relevant)
└── Data
├── Subfolder
│ ├── Other files (not relevant)
│ └── Sub-Subfolder
│ ├── Data File
│ ├── Data File
│ └── ...
├── Subfolder
│ ├── Other files(not relevant)
│ └── Sub-SubFolder
│ ├── Data File
│ ├── Data File
│ └── ...
└── ...
Only having to put things in the right folder when you change something.

## Slide 38: Data File Example