## Slide 1: Staying Cool: the Thermoelectic Cooling of SiPMs
Julien Hacot-Slonosky
Supervisor: Thomas Brunner
CASST 2024
Contact: julien.hacot-slonosky@mail.mcgill.ca

## Slide 2: The nEXO Experiment
A proposed search for the hypothetical neutrinoless double beta decay (), proposed to be at SNOLAB
  5 tonnes LXe enriched to 90% 136 Xe
  The time projection chamber houses ~104 silicon photomultipliers (SiPMs) to detect scintillation light from
Projected half-life sensitivity of 1.35x1028 years at 90% C.L.
Characterize how silicon photomultipliers (SiPMs) act at LXe temperatures
https://nexo.llnl.gov/nexo-overview

## Slide 3: SiPM Characterization at Low Temperatures
Silicon photomultipliers (SiPMs) in nEXO will work to detect scintillation light from decay events at LXe temperatures (~ -100).
One part of testing SiPMs is measuring their sensitivity to a single photon at low temperatures, and so we want to suppress the dark count rate.
-40 is a low enough temperature where the dark counts can be neglected.
Can reach -40 much more easily with thermoelectric coolers (TECs).

## Slide 4: How Do Thermoelectric Coolers Work?
TEC employ the Peltier effect:
  When current passes through two dissimilar semiconductors (n-type and p-type), a temperature gradient forms across the junctions, depending on the direction of the current.
TE coolers pass direct current from N-type to P-type semiconductors.
Modules are made of many semiconductors arranged thermally in parallel, but electrically in series.

## Slide 5: How do TECs Work?
Modules are made of many semiconductors arranged thermally in parallel, but electrically in series.
https://tetech.com/faqs/#15
Direction of heat moved
Direction of current applied

## Slide 6: Initial Tests
1 TEC pressed between a pc chip water cooling block and an aluminum thermal load.
Closed loop cooling
Aluminum block
TEC
PC water cooling block
Stainless steel bolts
12V water pump
water reservoir
cooling module
Thermistor

## Slide 7: Initial Tests
The original setup works:
  As the water temperature increased, so did the temperature of the aluminum block.
  Recycled water from closed loop decreases the amount of heat able to be pulled away.
  Single unit gave a constant .

## Slide 8: Upgrading the System
Two avenues for improvement:
  Better heat sink
  More heat moved
Better heat sink:
  Closed loop recycles warm water with limited heat dissipation
  Open loop from the building chilled water supply allows for cooler water at constant temperature
More heat moved
  Using more units allows for greater
  Stacking units loses efficiency quickly

## Slide 9: The Trouble With Stacking TECs
The thermal load on an individual TEC increases the further down the stack it is until it cannot cool the load any further.
Load
Unit 1
Unit 2
Unit 3
Heat Sink
Notes: Individual units produce their own heat as they operate
Units below must move the heat leaking from the units above as well as the heat to cool the load
This effect cascades until no more heat is moved from the lower units

## Slide 10: The Trouble With Stacking TECs
8 V
x 3 A = 24 W used
For first unit 24 W used + 13 W pumped = 37 W total
6 V
x 3 A = 18 W used
For second unit 18 W used + 13 W pumped = 31 W total
In total, 18 W used + 21 W used = 39W total for a
Quickly diminishing returns

## Slide 11: How to Stack TECs
3-stack
  All thermally in series
  First two electrically in series
  Bottom in parallel with first two
Bottom receives twice the current to deal with the extra heat load
Unit 1
Unit 2
Unit 3
Vin
GND

## Slide 12: First Trials
Tested a 3-stack with open loop cooling with water from the tap
Clearly something is not working as intended…

## Slide 13: Back to Basics
The 3-stack method only works if all the units are the same, these were not…
Replaced the 3-stack with one TEC1-12704k10 unit
Replaced the stainless steel bolts with plastic bolts
Used open loop water cooling
Aluminum block
TEC1-12704k10
Water Cooling Block
14.90 V, 3.65 A
GND
Water in
Water out
Plastic bolts

## Slide 14: Back to Basics
The open loop cooling is much better than the closed loop cooling
Using a thermally insulating layer between the hot and cold side also improves performance
!

## Slide 15: Latest Attempt With 3-Stack
Stacked 3 TEC1-12704k10
Used 3D printed spacers between the bolts
Used open loop cooling
Still only -11 with the 3-stack

## Slide 16: Moving Forwards
Find better ways to thermally isolate the load from the environment, hot side
Prevent the buildup of ice crystals that will envelop the SiPM
Incorporate the open loop cooling with the building chilled water supply

## Slide 17: Acknowledgements
Professor Thomas Brunner
And all the McGill Physics department technical staff

## Slide 18: Extra Slides

## Slide 19: The Trouble With Stacking TECs
Laird Thermal Systems, Multistage series electric cooler https://www.lairdthermal.com/datasheets/datasheet-MS2-049-14-14-15-15-11-W8.pdfr