## Slide 1
The HALO Supernova Neutrino Detector
Tom Sonley
Staff Scientist, SNOLAB
Oct 1, 2025

## Slide 2
HALO – The Helium And Lead Observatory
A “SN detector of opportunity” / An evolution of LAND – the Lead Astronomical Neutrino Detector,
C.K. Hargrove et al., Astropart. Phys. 5 183, 1996.
Helium – availability of 3He neutron detectors from the final phase of SNO
Lead – high -Pb cross-sections, low n-capture cross-sections, complementary sensitivity to water Cerenkov and liquid scintillator SN detectors, available from decommissioned cosmic-ray station
Review: E. Caden et al. Canadian Journal of Physics. 103(8): 763-774

## Slide 3
HALO Neutrino Detection
Neutrinos interact on lead, producing neutrons
  1 or 2 with energy thresholds
Neutrons thermalize
Neutrons capture on 3He
  τ ~ 200 us
Neutron counting only
No prompt signal
15 mHz background neutrons
  1/minute

## Slide 4
Multi-Messenger Astronomy with Supernovae
Nakamura et al,
MNRAS 161, 3296 (2016)
Galactic Supernova Rate is 1.6  0.5 per Century
Rozwadowska, Vissani, & Cappellaro, New. Astron. 83, 101498 (2020)

## Slide 5
Multi-Messenger Astronomy with Supernovae
Nakamura et al,
MNRAS 161, 3296 (2016)
Galactic Supernova Rate is 1.6  0.5 per Century
Rozwadowska, Vissani, & Cappellaro, New. Astron. 83, 101498 (2020)

## Slide 6
Flavour Complementarity
ne CC
NC
ne CC
Strong threshold dependence
(w/o Gd)
Low thresholds see NC coherent scattering
CC:
NC:

## Slide 7
HALO Details
Re-using SNO’s “NCD” 3He proportional counters
5 cm diameter x 3m and 2.5m in length, ultra-pure CVD Ni tube (600 micron wall thickness)
2.5 atm (85% 3He, 15% CF4, by pressure)
Four detectors with HDPE moderator tubes in each of 32 columns of lead rings
128 counters (368 m) paired for 64 channels of readout
Roughly 12” of water as reflector/shielding around sides
79 tonnes of lead

## Slide 8
3He Proportional Tubes
573 keV
= 900 ADC
191 keV
= 300 ADC
B. Beltran et al New J. Phys. 13, 073006 (2011)

## Slide 9
Electronics
Simple + Stable Readout:
AC Coupled pre-amplifiers on each channel
~2kV HV tuned to put peak at 1200 ADC counts
Discriminators set to detect 5 Hz of beta/gamma events total
Electronic calibration pulses injected at pre-amplifier on each channel every 4-8 hours
Highly redundant system:
2 DAQ machines trade off every 3 days (hot spare)
Separate HV + ADCs for right and left halves
Robust email alerts
Monitoring shifts require 10 minutes/day
95% of issues can be resolved remotely
ADC Channel
Counts (AU)
Current Run
2016 Calibration

## Slide 10
Calibration Method
Use distortion of multiplicity distribution to fit efficiency
20 Bq 252Cf / 250Cf source
~ 4 neutrons per fission
192 locations
~ 5 days of livetime
C. Bruulsema MSc Thesis, 2017
Centre
48.9 ± 0.4%
Edge
20.9 ± 0.4%

## Slide 11
Calibration Results
Average efficiency of 28% for neutrino-induced neutrons.
C. Bruulsema
Efficiency at Centre Depth
Efficiency vs Depth

## Slide 12
Roughly 10 neutrons @ 10 kpc
LS220-z9.6co spectrum
@ 10 kpc for HALO-1kT design
HALO has ~10 x less target
 CC 2n
 NC 2n
 CC 1n
 NC 1n
A. Gallo Rosso
Total HALO-1kT
neutrons

## Slide 13
J. Brau
4 – Neutron Trigger Probability
15 mHz background neutrons 2 second window
τ >> 200 us (non-spallation)
Coincidence Number | Rate
2 | 2 / hour
3 | 1 /day
4 | 1 / month
C. Bruulsema
High Energy Spectrum
Medium Energy Spectrum
Low Energy Spectrum

## Slide 14
Spallation Neutron Multiplicity

## Slide 15
Detector Status
Full detector being read-out since May 8th 2012.
Daily shift-taking since July 27th 2012.
Burst trigger implemented and connected to SNEWS since October 8, 2015
Full calibration done with and without front shielding wall April 2016
DAQ overhaul in 2020
98.7% Livetime July 2013 – Aug 2021
* Timestamps less reliable before June 2013
Year | 2013* | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 
Livetime (%) | 98.05 | 98.27 | 98.24 | 96.47 | 99.37 | 99.59 | 99.36 | 99.19 | 99.58 | 99.49 | 99.2 | 99.2 | 

## Slide 16
SuperNova Early Warning System
K. Scholberg 2023
Server receives independent reports from many experiments
Issues Alerts if multiple experiments are in coincidence
SNEWS 1.0 in operation since July 1, 2005
SNEWS 2.0 in testing. Whitepaper: https://arxiv.org/abs/2011.00035

## Slide 17
Mini-HALO Cross-Section Measurement
Lead
Low EBC graphite
HDPE / borated HDPE
Muon veto
 CC 2n
 NC 2n
 CC 1n
 NC 1n
A. Gallo Rosso

## Slide 18
Mini-HALO Cross-Section Measurement
Lead
Low EBC graphite
HDPE / borated HDPE
Muon veto
 CC 2n
 NC 2n
 CC 1n
 NC 1n
A. Gallo Rosso
HALO ROI
COHERENT Collaboration, arXiv:2109.11049
Neutrino Flux from the Spallation Neutron Source (ORNL) Stopped Pion Beam

## Slide 19
Future Proposal: HALO-1kT
28 x 28 array of 5.5 m-long, 5 cm-diameter 3He counters
8 mm-thick Polystyrene tubes around counters
1000 tonnes of Lead
30 cm graphite reflector (grey)
30 cm water shielding (blue)

## Slide 20
Commissioned in May 2012
Connected to SNEWS in October 2015
Calibration Run Spring and Summer 2016
1st Maintenance Campaign Completed 2021
> 95% live fraction for 12 years
  >99% for last 8 years
No supernova neutrino bursts detected yet…
Funded by:
HALO Status