## Slide 1: CUTE: Cryogenic, Underground and Totally Epic
By – Dev Chauhan
Supervisor – Matthew Stukel
1

## Slide 2: Presentation Path
2
Dilution Fridge
Specialized Facility
CUTE

## Slide 3: What is CUTE? 1
Cryogenic Underground TEsting facility
2

## Slide 4: An extraordinary underground facility
CUTE
3
Built for ultra low background
detection and measurements
Originally commissioned as a
Testing facility for SuperCDMS
detector tower testing

## Slide 5: Dilution Fridge 2
The Heart of CUTE
4

## Slide 6: CUTE fridge
Dry Dilution Refrigerator
Reaches temperatures as low as 12 mK
This is over 100 times colder than outer space(2 K)
5

## Slide 7: Stage 1 and 2: Pulse Tube cooling
Modern "Dry" Systems:
Eliminate need for liquid helium pre-cooling
Operating Principle:
Oscillating pressure waves and gas displacement
with no moving parts at cold end
Multi-Stage Cooling:
Provides 50K, 4K stages before dilution unit
Key Advantages
No liquid cryogens required for precooling
Simplified operation and maintenance
Cold Plate
6

## Slide 8
El
Helium
7
+
+
-
-
+
+
-
-
Property | Helium-3 (³He) | Helium-4 (⁴He)
Number of Neutrons | 1 | 2
Natural Abundance | ~0.0001% of helium on Earth | ~99.9998% of helium on Earth
Quantum Statistics | Fermion (spin-½) | Boson (spin-0)
Boiling Point at 1 atm | 3.19 K | 4.22 K
Vapor pressure at 0.7 K | ~120 Pascal | Negligible
Mass | 3.016 u | 4.0026 u
Cost | ~2700$/Liter | ~50$/Liter

## Slide 9
The Helium-3/Helium-4 Mixture
Below 0.87 K, ³He-⁴He mixture separates into two phases
Concentrated phase:
Nearly pure ³He
Dilute phase:
Contains 6.6% ³He in ⁴He
Key Thermodynamic Principle:
1. At He-3 concentrations below 6.6%, He-3 atoms exist in a lower energy state in the dilute phase than in the concentrated phase
2. The enthalpy of He-3 is higher in the dilute phase than in the concentrated phase
8

## Slide 10: Mixing Chamber
1. The still removes He-3 from the dilute phase
(We will get to how in the next slide)
2. He-3 from the Concentrated phase replaces
the He-3, absorbing energy(heat) in the process
3. This process repeats to reach temperatures as low as 12 mK
He-4
He-3
To Still
Concentrated phase
Dilute phase
Heat
9

## Slide 11: Still stage (0.7 K)
2. The He-3 is replaced from an He-3
From the Mixing Chamber
3. The process keeps on repeating
He-4
He-3
Vapor pressure at 0.7 K | Negligible | ~120 Pascal
From
Mixing Chamber
Heater
Pump
He-3 Vapour
10
1. At 0.7 K, ~all of the vapor is He-3

## Slide 12
Putting it together
11
He-3

## Slide 13
Gas Handling System
Circulation Pumps
Pumps maintain ³He flow through the dilution circuit
Purification System
Charcoal cold traps remove impurities from circulating ³He
Pressure Control
Regulates pressure and flow rates for optimal cooling performance
Storage Tanks
Store ³He inventory when system is warm or during maintenance
Gas Purity Requirements
He-3 purity is critical for performance. Even small amounts of impurities (⁴He, air, water vapor) can block circulation lines and reduce cooling power.
12

## Slide 14: Facility 03
What makes CUTE unique
13

## Slide 15: A unique low-background facility
14
Built to reduce background noise
Has a specialized class -100 cleanroom
with a radon reduced environment
Has special vibration dampers installed to minimize mechanical noise

## Slide 16: Multiple layers of shielding
Fridge
3
Water
Layer
Material
Shields
against
Neutrons
2
Lead
Gamma
1
Mu-metal
Magnetic fields
15

## Slide 17: A unique low-background facility
16
Built to reduce background noise
Has a specialized class -100 cleanroom
with a radon reduced environment
Has special vibration dampers installed to minimize mechanical noise
Lead and Mu-Metal shield
PE Neutron
shield
Lead shielding

## Slide 18: Calibration systems
Gamma Calibration system
37 kBq Ba-133 source
Neutron Calibration system
37.5 kBq Ca-252 source
17

## Slide 19: Run history
Past
Supercdms tower testing
HVeV detector run
Present
Qubit
Future
TBD
18

## Slide 20: Remarks
Nearly a year at the CUTE facility has been an extraordinary journey of discovery. Working with the project has not only expanded my technical expertise but also ignited a deeper passion for experimental physics. The knowledge gained here—from theoretical understanding to practical problem-solving—has been truly invaluable. I extend my heartfelt appreciation to everyone who made this incredible learning opportunity possible.
19

## Slide 21: Thank you!!
To my supervisor Matthew Stukel
To everyone at the CUTE team, including Vijay, Marco, Andy and Wolfgang
To all of my fellow students, current and past, for an amazing term!
I would like to thank SNOLAB
20

## Slide 22: References
Engert, Jost & Fellmuth, B. & Jousten, Karl. (2007). A new 3He vapour-pressure based temperature scale from 0.65 K to 3.2 K consistent with the PLTS-2000. Metrologia. 44. 40-52. 10.1088/0026-1394/44/1/006.