## Slide 1: Particle Tracking and Event Reconstruction using Gas Electron Multipliers for DarkLight
Huajian (Andy) Yang
NSERC COOP at TRIUMF

## Slide 2: Dark Matter a 🥜
If DM is a particle, what are its properties?
How does DM interact with the standard model?
We are trying to solve this
(Dark Matter in a Nutshell)
10.3367/UFNr.0182.201201a.0003
From NASA
Notes: Dark Matter was first measured in galaxy rotation curves
Accounts for alot of the universe
Humans are curious people
We want to ask questions

## Slide 3: DarkLight
Lepton based dark boson search experiment at TRIUMF
Mass Spectrometers
Gas Electron Multipliers (GEM) x2
Trigger Scintillators
Incoming beam
Notes: Particle scattering experiment to conduct a resonance search for an X17-like boson
Aim to detect the process described on the left
(Explain Feynman diagram)
(Explain experiment diagram)
GEMs used to reconstruct tracks
Tracks used to determine momentum and reconstruct mass of parent particle
Conduct resonance search in mass spectrum

## Slide 4: Gas Electron Multipliers (GEMs)
Some Terminology (used later):
  Hit: The event that a particle passes through a GEM
  Cluster: The collection of readout channels that are “lit up” by a hit
Notes: Quick detour on explaining how detector works
GEMs are very important for darklight
Use them for track reconstruction
Has a Cathode and an anode, filled with a gas that particles can ionize
Particles drift through multiple multiplying layers,
Anode is a wire grid at the bottom, which collects charge

## Slide 5: DarkLight Simulation/Analysis Framework
Monte Carlo Simulations
Data Analysis
(Oversimplified)
What we will be talking about today
Notes: Important simulate process to get rough idea of analysis
(Explain framework)
G4 Simulation -> simulate detector readout -> analyze data -> get mass
What I work on
simulating GEM readout Locating and detecting hits in GEMs reconstructing particle tracks

## Slide 6: GEM Data Analysis Pipeline
Cluster identification
Hit Reconstruction
Track Reconstruction
Digitized GEM Signal
Mass Recon
Identify hits from readout channels
Extract hit positions from clusters
Trigger Data
Real Experimental Data
Notes: Cluster identification locates which channels belong to signal left by particle track
Hit extracts the precise location of where the track is in the middle of the GEM from multiple channels
Track reconstruction combines trigger hits and GEM hits to construct tracks

## Slide 7: Cluster Identification Process
Convoluted
Gaussian Convolution
Digitized Signal
Position Reconstruction
Peak Finding
Identified Cluster Size
Use Channel Gaussian
Use mm Gaussian
Increases Signal to Noise
Gaussian size optimized for multitrack resolution
Uses dynamic thresholds
Parameters tuned for detecting cluster width and multitrack accuracy
Channels
Readout
Notes: Digitized signal from top left
Passes through convoluted chi2 test. Increases SNR and detects gaussian peaks
Passes through another Gaussian convolution which helps increase the multitrack resolution of the peak finding algorithm.
- means the peak finder can better distinguish which peaks belong to which clusters
The peak finding algorithm uses the convoluted signal and decides where the cluster is and how wide the cluster is
Sends info to position recon

## Slide 8: Position Reconstruction
Use Charge Centroid Method
Can get to submillimeter accuracy
Identified Cluster Size
Take weighted average between green markers
Counts
Notes: Tracks in darklight can “light up” alot of readout channels (4-6mm worth of readoutchannels)
Need to get to <1mm accuracy
Because readout distribution almost follows uniform, can simply take weighted average

## Slide 9: Track Reconstruction
Connect all hits between two GEM layers
Filter out any tracks that dont have corresponding trigger hits
Simple & fast reconstruction
Does not need very sophisticated algorithm due to low event rate
High angular and position resolution
Positron Side

## Slide 10: Summary
Perhaps the new boson will shine light on SM and dark matter interactions
Reconstruction of particle tracks by GEMs is crucial in accurately measuring and finding the dark boson
Accurate mass reconstruction can be acheived
Reconstructed Mass

## Slide 11: DarkLight Timeline
May
July
August
October
2026+
Installation
Beam Commissioning
Commissioning Detectors
Data taking
Analysis
Everything is sitting in a beamline at TRIUMF
Undergoing beam commissioning
Will be taking beam very soon!
Notes: Experiment already deployed at TRIUMF (Installed from may to June, currently doing beam commissioning)
We are very excited to be taking data soon
Hope in near future hear more interesting results from our collab

## Slide 12: Thank you Merci
Follow us @TRIUMFLab
www.triumf.ca

## Slide 13: X17 Anomaly
Initially discovered by ATOMKI group
atoms bombarded with a proton beam
Measured angular distribution of caused by internal pair production
Unexpected pair production bump at ~
Can be explained by a new neutral axial-vector boson ~17MeV
Similar results confirmed in , ,
doi.org/10.1140/epjc/s10052-023-11271-x
https://doi.org/10.1103/PhysRevLett.116.042501
Needs independent confirmation
If there is an X17-like boson, could it couple to dark matter?
DarkLight Lore/Motivation
Notes: Assume the audience is semi-familiar with particle physics and have heard of dark matter
Get

## Slide 14: Other Experimental Efforts
PADME
MEG-II
Did not see X17 signal
Saw X17 Signal with

## Slide 15: Expected Signal
GEMs reconstruct tracks
Momentum of calculated through tracks
Mass of parent particle reconstructed
Expect a bump over the mass of dark boson
Background from photon coupling

## Slide 16: GEM Digitization
Initially done in Garfield++
A faster and simpler script was made for generating showers
The digitization script accounts for angle of impact and smear of tracks over readout
Spectrometer
~5mm
Arb. Units
Channel #
Notes: Digitization script simulates what each readout channel should readout
Showers inside GEMs initially done by Garfieldpp
Feature of script is that it accounts for impact angle of tracks