## Slide 1: Detecting the unseen: Neutron unfolding with Helium-3 counters
Kishan Chaudhary
Undergraduate Research Assistant, SNOLAB Supervisor: Dr. Ian Lawson CASST 2025

## Slide 2: Introduction:
Ambient neutrons a background for SNOLAB experiments:  Limit detector sensitivity of PICO, DEAP, SUPERCDMS, SNO+
Objective:
 Prepare method and analysis to measure neutron counts in range 0 to 11 MeV.
Notes: Use unfolding along with moderators to detect higher energy neutrons(up to 11 MeV).

## Slide 3: Helium-3 counters: Neutron detection
Fig: PNH Helium-3 proportional counter tube. Image credit: Mirion Technologies

## Slide 4: Helium-3 counters: Neutron detection
Fig: Neutron capture diagram
Helium-3
Triton(H-3)
K.E. 191 keV
Proton(H-1) K.E. 573 keV
Fig: PNH Helium-3 proportional counter tube. Image credit: Mirion Technologies
Slow neutron

## Slide 5: Helium-3 counters: Neutron detection
Fig: Neutron capture diagram
Fig: Simplified neutron counting flow diagram
Ionized charges
Pre-Amplifier
Amplifier
Slow neutron
Helium-3
Triton(H-3)
K.E: 191 keV
Proton(H-1) K.E: 573 keV
Fig: PNH Helium-3 proportional counter tube. Image credit: Mirion Technologies

## Slide 6
Limitation of Helium-3:
Slow neutrons only
Fig: Cross-Section plot for He-3 and He-4 interactions (Piscitelli et.al, Eur. Phys. J. Plus 135, 577, 2020)
Cross-section (barns)
Energy (eV)
Notes: r^-1 electric field, electron drift, high voltage near wires, charge pairs multiply proportionally, UG

## Slide 7
11 MeV
0.1 MeV
0.025 eV
0
Limitation of Helium-3:
Slow neutrons only
Slow neutrons
Epithermal neutrons
Fast neutrons
How to measure 0 - 11 MeV neutron counts with a detector that only detects slow neutrons
Notes: r^-1 electric field, electron drift, high voltage near wires, charge pairs multiply proportionally, UG

## Slide 8: How do we detect fast neutrons: Slow Them down!
Fast neutrons + scattering  Slow neutrons (Moderation: M. Joyce (Ed.), Nuclear Engineering)
Best moderation materials: Hydrogenous materials, example polyethylene and water

## Slide 9: How do we detect fast neutrons: Slow Them down!
Fast neutrons + scattering  Slow neutrons (Moderation: M. Joyce (Ed.), Nuclear Engineering)
Best moderation materials: Hydrogenous materials, example polyethylene and water
Fig: 2-D Neutron scattering tracks in a polyethylene brick using GEANT4
Neutron source (AmBe)
Polyethylene brick
Neutron tracks

## Slide 10: How do we detect fast neutrons? Moderation Cases
The Idea:
Use multiple polyethylene moderation setup
Fast Neutrons  Slow Neutrons  Detect
Polyethylene thickness ∝ Neutron’s final energies
But how do we reconstruct the source spectrum?
Moderation Cases
Bare(No moderation)
1-inch Polyethylene
2-inch Polyethylene
3-inch Polyethylene
4-inch Polyethylene
5-inch Polyethylene

## Slide 11: Moderation cases:
Moderation Cases
Bare(No moderation)
1-inch Polyethylene
2-inch Polyethylene
3-inch Polyethylene
4-inch Polyethylene
5-inch Polyethylene
Bare
1-inch
2-inch
3-inch
4-inch
5-inch
Neutron source
Polyethylene

## Slide 12: Detector slow neutrons count matrix:
Bare
1-inch
3-inch
4-inch
5-inch
Count Matrix (for 6 moderation cases)
2-inch

## Slide 13: What we need:
Bare
1-inch
2-inch
3-inch
4-inch
5-inch
Source Counts Matrix (for j energy bins in 0-11 MeV)

## Slide 14: How Do We Detect Fast Neutrons? Response
Bare
1-inch
2-inch
3-inch
4-inch
5-inch
Response Matrix (for 6 moderations and
j energy bins)

## Slide 15
How Do We Detect Fast Neutrons: Unfolding
Counts in Detector (C)
Response (R)
Neutron Source Counts ()
Unfolding Algorithms

## Slide 16: Test:
Calculate matrix “R” (using GEANT4)
Measure counts for AmBe “C” (using GEANT4)
Unfolding: Predicted AmBe counts “S
Check results
Find AmBe Spectra using unfolding algorithm:
Check simulations validity

## Slide 17
Fig: GEANT4’s neutron capture energy deposition with 10 keV gaussian noise
Check simulations validity

## Slide 18
Fig: GEANT4’s neutron capture energy deposition with 10 keV gaussian noise
Fig: Experimental energy deposition data (Peplowski et al., NIM A, 982, 164574, 2020)
Check simulations validity

## Slide 19
Fig: Response plot for the AmBe test
Calculate “R” (using GEANT4)
Check Simulations validity

## Slide 20
Fig: Response Plot from Yang-Yang laboratory for BSS (Yoon et al., Astroparticle Physics, 126, 2021)
Fig: Response plot for the AmBe test
Calculate “R” (using GEANT4)
Check Simulations validity

## Slide 21
Calculate “R” (using GEANT4)
Measure “C” for AmBe (using GEANT4)
Check Simulations validity
From 10 Million event run(AmBe) Equivalent to ~44 hours of actual AmBe run

## Slide 22
Response (GEANT4)
Use unfolding algorithm
Output:
(Predicted source counts)
Counts (GEANT4)
Calculate “R” (using GEANT4)
Measure “C” for AmBe (using GEANT4)
Unfolding: Predicted AmBe counts “S
Check Simulations validity

## Slide 23
Check results!
Calculate “R” (using GEANT4)
Measure “C” for AmBe (using GEANT4)
Unfolding: Predicted AmBe counts “S
Check simulations validity
During the test period: The AmBe source emitted 10 000 000 fast neutrons
The algorithm predicted 9 893 254 fast neutrons, about 99%! Takeaway: The Helium-3 counter successfully counts for fast neutrons!
GRAVEL algorithm results:

## Slide 24
Check results!
Calculate “R” (using GEANT4)
Measure “C” for AmBe (using GEANT4)
Unfolding: Predicted AmBe counts “S
Check simulations validity
Fig: Unfolded neutron source spectra (6 bins)
Fig: Actual AmBe spectra (6 bins)
0
0.025 eV
0.1 MeV
11 MeV
Slow neutrons
Epithermal neutrons
Fast neutrons

## Slide 25: Test complete:
Results: Can “see” the fast neutrons But can't tell apart their initial energy accurately
Calculate matrix “R” (using GEANT4)
Measure counts for AmBe “C” (using GEANT4)
Unfolding: Predicted AmBe counts “S
If sufficient: Success!
If not-sufficient: Try again!
Check simulations validity

## Slide 26: Summary:
In 4 months, prepared and tested a method to detect 0-11 MeV neutrons using point source.
Continuing the project in Fall term.
Ultimate objective: Measure ambient neutron flux using Neutral Current Detectors in 0-11 MeV.

## Slide 27: Thank you for listening!
Special Thanks to: Thomas Sonley: Unfolding advisor Ian Lawson and Steffon Luoma: Supervision Vijay I., Arina, Abhipsha, Peter, Dimpal, Keegan, Bilal

## Slide 28: Questions?

## Slide 29
Gamma-Neutron Overlap
Limitations of NCDs:
Slow neutrons only
 Background-neutron overlap
Fig: Experimental AmBe data, background overlap with neutron capture data
Gamma Backgrounds
Neutron capture events
Counts
Energy (keV)
Notes: r^-1 electric field, electron drift, high voltage near wires, charge pairs multiply proportionally, UG

## Slide 30
Fig: No polyethylene Geometry (GEANT4)
Fig: 2inch Polyethylene Geometry (GEANT4)
Fig: Picture of the Helium-3 Counters
Calculate “R” (GEANT4)

## Slide 31
Fig: Experimental Data, 3-inch Polyethylene
Fig: GEANT4’s triton and proton energy deposition per event with 10 keV gaussian noise
Energy (keV)
Counts
Calculate “R” (GEANT4)

## Slide 32: Neutral Current Detectors: Helium-3 Counters:
Custom Counters, used in SNO experiment.(Amsbaugh et al., 2007)
cross-section dependance, negligible for fast neutrons.
Gamma interference, can either: 1). Make a cut to remove gammas(lose neutron efficiency) or 2). Subtract background

## Slide 33: How Do We Detect Fast Neutrons: Convolution
Neutron Source Flux
Response: Moderation effects, Geometry, Detector intrinsic Efficiency
Detector’s Neutron Counts
(Convolution)

## Slide 34: How Do We Detect Fast Neutrons: Convolution
Neutron Source Flux
Response: Moderation effects, Geometry, Detector intrinsic Efficiency
Detector’s Neutron Counts
(Convolution)
Detector’s Neutron Counts
Response: Moderation effects, Geometry, Detector intrinsic Efficiency
(De-Convolution)
Neutron Source Flux

## Slide 35: De-Convolution Unfolding
The neutron convolution is governed by Fredholm Integral (first kind, ill-posed). Binned or Discretized version is a linear algebra problem(ill-imposed kernel matrix).
“Unfolding” problem, requires algorithms to solve un-determined linear equations.

## Slide 36: Unfolding using GRAVEL:
Requires algorithms to find suitable solutions for C and R.
Example, GRAVEL

## Slide 37: GEANT4(11.1.1) simulation:
Physics list: HadronElasticPhysicsHP, G4HadronPhysicsQGSP_BIC_HP, G4IonPhysicsXS, G4StoppingPhysics, ElectromagneticPhysics, GammaNuclearPhysicsLEND(LEND_GND1.3_ENDF.BVII.1), G4DecayPhysics, G4RadioactiveDecayPhysics
Tracking: Sensitive Volume: Inner Tube(He-3) Physical Volume, track individual tritons(use fStopAndKill) on every hit!
Energy Deposition: Edep from Tritons and Protons summed until event ends.

## Slide 38
Fig: GEANT4’s Triton and Proton Energy Deposition per event
Fig: Experimental low background data (Peplowski et al., NIM A, 982, 164574, 2020)
Check simulations validity

## Slide 39
Fig: GEANT4’s neutron capture energy deposition with 10 keV gaussian noise
Fig: Experimental energy deposition data (Peplowski et al., NIM A, 982, 164574, 2020)
Check simulations validity

## Slide 40: References:
[1] Piscitelli, F., Mauri, G., Laloni, A. et al. Verification of He-3 proportional counters’ fast neutron sensitivity through a comparison with He-4 detectors. Eur. Phys. J. Plus 135, 577 (2020). https://doi.org/10.1140/epjp/s13360-020-00600-8
[2] Joyce, M. (2018). Chapter 6 – Moderation. In M. Joyce (Ed.), Nuclear Engineering (pp. 111–127). Butterworth-Heinemann. https://doi.org/10.1016/B978-0-08-100962-8.00006-8
[3] Peplowski, P. N., Yokley, Z. W., Liebel, M., Cheng, S., Elphic, R. C., Hoogerheide, S. F., Lawrence, D. J., & Nico, J. S. (2020). Position-dependent neutron detection efficiency loss in 3He gas proportional counters. Nuclear Instruments and Methods in Physics Research Section A, 982, 164574. https://doi.org/10.1016/j.nima.2020.164574 [4] Yoon, Y. S., Kim, J., & Park, H. (2021). Neutron background measurement for rare event search experiments in the YangYang underground laboratory. Astroparticle Physics, 126, 102533. https://doi.org/10.1016/j.astropartphys.2020.102533
[5] Amsbaugh, J. F., Anaya, J. M., Banar, J., Bowles, T. J., Browne, M. C., Bullard, T. V., Burritt, T. H., Cox-Mobrand, G. A., Dai, X., Deng, H., et al. (2007). An array of low-background 3He proportional counters for the Sudbury Neutrino Observatory. Nuclear Instruments and Methods in Physics Research Section A, 579(3), 1054–1080. https://doi.org/10.1016/j.nima.2007.05.321