## Slide 1: The CUTE Way to Detect Neutrons Brianna Liz Supervisor: Prof. Matthew Stukel
Notes: If you’ve ever tried to hear a whisper in a noisy room, you know how hard it is to pick out something rare and faint from all the background chaos. At SNOLAB, we’re trying to hear some of the faintest ‘whispers’ in the universe but the ‘noise’ comes from particles like neutrons. So we go somewhere super quiet… two kilometers underground… and then bring out some very clever tools to find them

## Slide 2
CUTE
What is it?

## Slide 3: Cryogenic Underground TEsting facility
Dry dilution fridge
Cleanroom
Ultra pure water
Dry dilution fridge
Notes: The full form of CUTE is Cryogenic undergroudn testing facitily and it is located 2 kilometers underground at SNOLAB. But CUTE isn’t a detector itself. Instead, it’s a testing ground for experiments like dark matter and qubits.
CUTE consists of a clean room, a dilution fridge, a big tank of ultra pure water.
Because it’s so far underground, CUTE is shielded from cosmic radiation. And to test detectors that are supposed to catch very rare signals, we need to make sure the environment is as “quiet” as possible—no noise, no heat, and no shaking. That’s why CUTE is designed to be very still and very cold. CUTE uses a dilution refrigerator, clever trick with helium-3 and helium-4 gases to reach mind-blowing temperatures—down to 12 millikelvin, or about -273°C.
Here’s a fun way to imagine that: if absolute zero is the coldest anything can possibly be, CUTE is just a hair’s width above that!
Formerly used for testing SuperCDMS dark matter detectors, CUTE now examines quantum chip performance in the absence of cosmic radiation.

## Slide 4
Neutron background at SNOLAB
Being underground doesn’t mean that we’re free of all radiation

## Slide 5
Neutron Sources At SNOLAB
1. Calibration Sources
2. Surrounding Rock/Shotcrete
Cf-252
(Alpha, n) reactions
Fission reactions

## Slide 6
42 He
10 n
End product: fast neutron
(Alpha, n) reactions
Reacts with elements like Carbon, oxygen and beryllium

## Slide 7
23592 U
23190 Th
42 He
Reacts with elements like Carbon, oxygen and beryllium
10 n
End product: fast neutron
(Alpha, n) reactions
Uranium in the rocks

## Slide 8
Fission reactions
23592 U
Lighter element
Uranium in the rocks
Lighter element
10 n
Neutron from other
reactions
10 n
10 n
10 n

## Slide 9
NEUTRON DETECTION
IT IS IMPORTANT WE DETECT THEM

## Slide 10
Importance of Neutron Detection At SNOLAB
1. Neutron signals similar to dark matter signals
2. Is the neutron background homogenous across the lab?
Different locations at
CUTE
Estimated flux :
4000 n/m2/day

## Slide 11
Current neutron detector
Kromek TN detector
Thermal
Li-6
SiPM
Upcoming neutron detector
S670e detector from Arktis
Fast and thermal
24 SiPMs
Li-6
180 bar He-4
Neutron Detector

## Slide 12
Fast neutron
He-4 nucleus in detector
How Arktis detects FAST neutrons
Detector wall
SiPM
Electronic board
The S-670e produces TTL pulses of different widths

## Slide 13
Fast neutron
He-4 nucleus in detector
Detector wall
How Arktis Detects FAST Neutrons

## Slide 14
Fast neutron
He-4 nucleus in detector
Detector wall
How Arktis Detects FAST Neutrons

## Slide 15
--------------------------->
Fast neutron
---------->
He-4 nucleus in detector
Detector wall
How Arktis Detects FAST Neutrons

## Slide 16
SiPM
Electronic board
The S-670e produces pulses of different widths
Scintillating light
How Arktis Detects FAST Neutrons

## Slide 17
Thermal neutron
Li-6 nucleus in detector
Detector wall
How Arktis Detects THERMAL Neutrons

## Slide 18
Thermal neutron
Detector wall
Li-6 nucleus in detector
How Arktis Detects THERMAL Neutrons

## Slide 19
---------->
High-energy alpha particle
--------------------------->
Triton nucleus
Detector wall
How Arktis Detects THERMAL Neutrons

## Slide 20
Scintillating light
SiPM
Electronic board
The S-670e produces pulses of different widths
How Arktis Detects THERMAL Neutrons
High-energy alpha particle

## Slide 21
How Do SIPMs & Electronics Know It’s a Neutron?

## Slide 22
Time over Threshold Parameter
Measures how long the signal amplitude stays above a certain offset (the “threshold”)
If the signal amplitude is tall and wide—possibly by a neutron
If it’s small and quick—possibly just noise or a gamma ray
Cuts can be set to determine the characteristic of the neutrons
The Time over Threshold (ToT) parameter

## Slide 23
How the detector knows it’s a neutron
Signal capture
Threshold check
Coincidence requirement
Decision
Each SiPM pair sends its signal to a discriminator
If signal > offset threshold  line is set to HIGH in Coincidence Unit
If 2 lines are high within 30 ns, ToT counter starts
If ToT > cut  likely a neutron  pulse produced
If ToT =< cut  not a neutron  no signal sent

## Slide 24
DISCRIMINATORS
COINCIDENCE UNIT
HIGH
HIGH
ToT CALCULATION COUNTER
Pulse produced based on ToT value
Simulation of neutron detection
24

## Slide 25
DISCRIMINATORS
COINCIDENCE UNIT
HIGH
HIGH
ToT CALCULATION COUNTER
Pulse produced based on ToT value
Simulation of Neutron Detection

## Slide 26
July 2025
Complete project review and approval
Initiate detector procurement
September 2025
Receive detector and conduct initial surface tests
Secure all required certifications
October 2025 – March 2026
Perform underground testing: begin in the low-background laboratory, followed by multiple locations within the CUTE facility
Arktis S670e Project Timeline

## Slide 27
How the neutron signal is read

## Slide 28
THANK YOu

## Slide 29
Camus, P., Corbett, J., Crawford, S., Dering, K., Fascione, E., Gerbier, G., Germond, R., Ghaith, M., Hall, J., Hong, Z., Kubik, A., Mayer, A., Nagorny, S., Pakarha, P., Rau, W., Scorza, S., & Underwood, R. (2024). CUTE: A Cryogenic Underground TEst facility at SNOLAB. Frontiers in Physics, 11, 1319879. https://doi.org/10.3389/fphy.2023.1319879
Arktis Radiation Detectors Ltd. (2018). Arktis S-670(e) detector series: Operating manual (Version 7, ID-No. AM0022). Zurich, Switzerland: Arktis Radiation Detectors Ltd.
Kelley, R. P., Murer, D., Ray, H., & Jordan, K. A. (2015). Analysis of the scintillation mechanism in a pressurized 4He fast neutron detector using pulse shape fitting. AIP Advances, 5(3), 037144. https://doi.org/10.1063/1.4916904
REFERENCES