## Slide 1: SNO+ DAQ Chain from Pulses to Analysis ready data
Mark Ward
SNOLAB Users meeting MAY 26, 2026

## Slide 2: The SNO+ Detector
2Km Underground (6000 mwe Shielding)
12m Acrylic Vessel
780T of organic liquid scintillator (LAB)
7000T UPW Shielding
Detector held down to the cavity floor via rope net
Stainless Steel PMT Support structure
9362 8inch Photomultiplier Tubes (R1408) providing 54% photocoverage
Outward looking muon veto.

## Slide 3: Physics Goals
Multi-Purpose neutrino physics detector
  Solar neutrinos
  Reactor neutrinos
  Geoneutrinos
Primary goal is a neutrinoless double beta decay search using Tellurium-130
  130Te selected for favorable Q value (2.53MeV) and natural abundance (34.08%)
  3.9 T of natural Tellurium, 1.3 T of target isotope
  Double beta lifetime measurement T1/2 ~8.2x1020 years
  Neutrinoless double beta decay mode 5 year sensitivity target of T1/2 ~2.1x1026 years

## Slide 4: How do we go from Physics to data
But what is the signal?
  In SNO+ we get Voltage pulses from PMTs
How do we define interesting?
  There are ~9400 PMTs, this is a lot of information
Do we save everything?
  No…
Get Signal from Detector
Is signal interesting?
Yes
Save Signal
PHYSICS!
WITNESS ME!
No

## Slide 5: In SNO+
Monolithic target
  Energy deposited in the LAB produces ionization and scintillation, this is our raw physics.
~9400 inward facing PMTs observe the Photons.
  Convert the photons into a readable electrical signal.
  Light yield of 330 PMT hits / MeV. (N.B. NOT photoelectrons!)
Determine if something happened worth recording.
  Most useful metric is ~ NHITS / Time window ~ dE/dT
SO lets go for a dive

## Slide 6: Divide up the channels
The deck area of SNO+ is not as tidy as shown in the diagram, also the support is baby blue.
9400 inward facing PMTs are divided into 19 crates
19 crates distributed among 11 Racks around the detector
Each crate divided into 16 ‘slots’ each with 32 channels
Each slot is composed of a PMT-interface Card and Front End Card
Each Front end card has 4 daughterboards, addressing 8 PMTs
A single Crate
Some LEDs even flash!

## Slide 7: From scintillation to ‘Event’ Under the water
Photon(s) produced by the detector are absorbed by PMTs, and an photoelectrons produced by the photoelectric effect
Photoelectrons are multiplied by the PMT
Induced signal travels along the HV cable toward the deck
pmt
HEX cell
e-
330 ‘hits’ / MeV
NOT
330 photons/Mev
(the glowing orb is not typical, its a lamp)

## Slide 8: From scintillation to ‘Event’ – To the Deck
Cables are bundled in groups of 8 and come through between the deck and the cavity wall.
Electronics Rack

## Slide 9: An example Crate

## Slide 10: An example Crate - The Test stand
Back Plane
with Sockets
Crate Trigger Card
XL3
3 Front end Cards
PMTIC Sockets

## Slide 11: Front End Card PMT Interface Card
TO/FROM PMT
Paddle Card
Daughter Board
Back Plane
Socket
4 HV relays

## Slide 12: From scintillation to ‘Event’ - PMT Triggers
TO/FROM PMT
Paddle Card
Daughter Board
Back Plane
Socket
4 HV relays

## Slide 13: From scintillation to ‘Event’ - Daughter Boards
Each Daughter Board deals with 8 channels in 2 lanes
On A threshold cross, we start TAC for that channel
The output is ESUMHI, ESUMLOW, N100 and N20 analog sums
Charge integration in two windows, Short…70ns (QHS) and long 400ns (QHL) and QHX (we ignore this one)
RAW PMT
x8
Start/Stop
Integrator
4 in
4 in
x2
x2
ESUMH
ESUML
ESUMH
ESUML
4ch
4ch
4ch
4ch
4ch
x8
Create N100 N20
8ch
8ch
N100
N20
TAC
Discriminator

## Slide 14: From scintillation to ‘Event’ - FEC level sums go to the backplane
TO/FROM PMT
Paddle Card
Back Plane
Socket

## Slide 15: From scintillation to ‘Event’ - Daughter Boards
Back Plane
Crate Trigger Card
XL3
3 Front end Cards
All FECs send ESUMH ESUML N20 N100 to the Crate Trigger card

## Slide 16: From scintillation to ‘Event’ - Analog Sum of whole detector!
Not one Unit, but 7 Master Trigger cards, (MTC/A*)
Analog sum each Crate Trigger Card output.
At this point, we have a final total analog sum of the whole detector in 10 different paths.
Here we have a final threshold applied which generates one final trigger pulse which we send to the Master Trigger Card / Digital+
n100 Threshold
Send to MTC/D+

## Slide 17: From scintillation to ‘Event’ - Make a trigger decision
Takes care of timing and synchronization
This card generates the Global Trigger!
This is based on which trigger paths are active on the MTC/A+ or from other sources.
Global trigger is sent back to the Crate trigger cards and distributed to each Front End Card
1996!!!!

## Slide 18: From scintillation to ‘Event’ – Form events on FECs
Each Front end Card gets signalled by the Global Trigger to save data to a buffer
Data Produced
TAC voltage ramp stops, giving the hit time relative to the global trigger
Short and Long charge integration data
Note if a hit doesn’t result in observing a Global Trigger The daughterboards will discard the data after 420ns

## Slide 19: From scintillation to ‘Event’ – Send hits to the Builder
We have Data on each FEC So how do we get it out?
THE XL3!
The XL3 checks the cmos data status on each FEC. If data is available the XL3 will read it out
Data travels along the backplane to the right
The brain of the XL3 is a FPGA and PPC processor which provides a tcp/ip interface and routes the data to the builder which will create an Event for each Global Trigger
  Event = Global Trigger ID, MTC/D clock time, Trigger Flags, GPS clock time, Digitized Trigger waveforms x3,
  PMT hit info = 3 Charge integrals, relative hit time and status per hit.
DONE!…. Next event…
XL3

## Slide 20: Example event

## Slide 21: In Step Run-Selection
We perform a set high level data processing on each run and classify the quality of the data based on what criteria it meets
In total there are 57 properties of the data that we look at and slot it into… We need to meet all/most conditions.
  Gold : Perfect as good as its going to get, All crates on and enough PMTs are working.
  Silver: Good… but more offline channels than gold
  Bronze: Crate off? No worries just not too many please.
  Nickel : Is the detector on and not going crazy? Cool!
N.B. – this is a gross over simplification.

## Slide 22: So coverage determines most of it?.... Yes… but also no.
  Gold/Silver/Bronze/Nickel largely fall into dqhl differences.
  dqhl – data quality high level
    Are trigger rates normal?
      Are we above pulse GT… (10Hz)
    Is timing in the detector alright?
      Is the clock ticking? Do we see any large clock jumps?
    Do we have enough PMTs on?
      Are any crates off?
      Are there any panel gaps that are too large?

## Slide 23: So coverage determines most of it?.... Yes… but also no… part 2
Some flags can cause us to fail runs outright…
Detector state
  Do we have blind flashers?
  Is data being written in an orderly manner?
  Is data piling up on the FECs?
  Is the detector able to count properly
  Are the FECs able to see the correct global trigger number.
  Are there any critical alarms active?

## Slide 24: So coverage determines most of it… fine… it’s a big part but still no
Did any crates randomly stop talking to the builder?
Is the run longer than 30 minutes
Is anyone on deck… hitting things?
Does the run belong to a runtype that should not be used for physics.
Do we see too many muon like events?
Did any FECs have an identity crisis?
Does someone just not think the run should pass for reasons they note in the shift report?
Im the FEC in 12/8 and I’m going to be a issue!

## Slide 25: Things that cause bad runs… Example 1 : PMT breakdown
When PMTs breakdown, they typically produce a lot of light in the detector, and a large amount of events.
This is ok and can be classified, if it’s a short burst.
Can raise an alarm
  Channel/daughterboard/slot going offline gets flagged daq side
  Sustained bursts can flood front end electronics, causing daq alarms
  Breakdowns can look like Muons, No… we didn’t get 1000 muons in a few seconds.

## Slide 26: Things that cause bad runs… Example 2 : Bad Data
It is possible for a Front End Card to ‘forget’ where it is in the detector.
  This can be due to a failing component on the card that causes its ‘reset on power on’ circuit to fire.
  The builder is able to tell when this happens and produces an alarm.
Im the FEC in 12/8 and Im suddenly going to tell the builder im actually in 0/0

## Slide 27: Things that cause bad runs… Example 3 : Mega bundles go bad
If a front end card produces a PMT ‘mega-bundle’ which makes no sense, the builder will raise an alarm, typically like the previous example, flagging bad data.
Typically words 1 and 3 are vital and will cause most of the issues if there are any
  Huge GTID jumps get flagged, if it occurs too much, the run will fail.
Can occur both front end and transferring information from the FEC to the XL3 to the builder.
If a FEC doesn’t receive a Sync16 or Sync24 flag it means the FEC is not recording GTID correctly data will go out of sync with respect o the detector – it will cause issues and gets flagged.

## Slide 28: Run Selection – The on going task for a mature DAQ
Run Selection and Data Quality monitoring is a on-going task
It changes as we uncover new and interesting ways we can define how good data is and what the DAQ does.
The local team is tasked with not only uptime, but producing analyzable data!
  The largest challenge we face is that of PMT coverage, and is completely dominated by environmental factors and our ability to mitigate it.
  The underground environment is harsh on electronics.
  The electronics is being pushed beyond its intended operation from SNO, which has, produced new and ‘interesting’ failure modes which require sometimes innovative solutions.
  Electronics older than many in this room is also a reality we need to deal with.
SNO+ has produced a flurry of publications over its run time thus far!