## Slide 1: SNOLAB Ambient Fast Neutron studies
Brianna Liz Binoy
Research Assistant, CUTE Supervisors: Dr. Matt Stukel

## Slide 2
Neutron background at SNOLAB
Being underground doesn’t mean that we’re free of all radiation
2

## Slide 3
Neutron Sources At SNOLAB
1. Calibration Sources
2. Surrounding Norite Rock & Shotcrete
Cf-252
(Alpha, n) reactions
Fission reactions
3

## Slide 4
23592 U
23190 Th
42 He
Reacts with elements like Carbon, oxygen and beryllium
10 n
(Alpha, n) reactions
Uranium in the rocks
4

## Slide 5
Neutron Sources At SNOLAB
(Alpha, n) reactions
Fission reactions
5
2. Surrounding Norite Rock & Shotcrete

## Slide 6
Fission reactions
23592 U
Lighter element
Uranium in the rocks
Lighter element
10 n
Neutron from other
reactions
10 n
10 n
10 n

## Slide 7
NEUTRON DETECTION
IT IS IMPORTANT WE DETECT and understand THEM
7

## Slide 8
Importance of Neutron Detection At SNOLAB
1. Neutron signals similar to dark matter signals
2. Is the neutron background homogenous across the lab?
8

## Slide 9
9
Neutron classifications | Energy
Cold energies | < 0.01 eV
Thermal | 0.01 eV – 0.3 eV
Epithermal | 0.3 eV-10 keV
Fast | 10 keV-20 MeV
Relativistic | > 20MeV
Neutron classifications
Notes: Spectrum

## Slide 10
NEUTRON DETECTOR
The ARKTIS FAST & Thermal NEUTRON DETECTOR
10

## Slide 11: Arktis S670e Detector
Made of stainless steel
Sensitive to fast and thermal neutrons
Fast neutrons: Pressurized Helium-4 gas & Thermal neutrons: Lithium-6 coating
    3 optically decoupled segments, each with 8 Silicon Photomultipliers
Arktis S670e Operation Manual
Notes: Talk to the slide more, point to the detector and show exactly where things are

## Slide 12
Fast neutron
He-4 nucleus in detector
Detector wall
How Arktis Detects FAST Neutrons
12

## Slide 13
Fast neutron
He-4 nucleus in detector
Detector wall
How Arktis Detects FAST Neutrons
13

## Slide 14
----------->
Fast neutron
------>
He-4 nucleus in detector
Detector wall
How Arktis Detects FAST Neutrons
14

## Slide 15
SiPM
Electronic board
produces pulses
Scintillating light
How Arktis Detects FAST Neutrons

## Slide 16
Thermal neutron
Li-6 nucleus in detector
Detector wall
How Arktis Detects THERMAL Neutrons
16

## Slide 17
Thermal neutron
Detector wall
Li-6 nucleus in detector
How Arktis Detects THERMAL Neutrons
17

## Slide 18
---------->
High-energy alpha particle
--------------->
Triton nucleus
Detector wall
How Arktis Detects THERMAL Neutrons
18

## Slide 19
Scintillating light
produces pulses
High-energy alpha particle
SiPM
Electronic board
How Arktis Detects THERMAL Neutrons
19

## Slide 20: How the signals are detected
Measures how long the signal amplitude stays above a certain offset (the “threshold”)
If the signal amplitude is tall and wide—possibly by a neutron.
If it’s small and quick—possibly just noise or a gamma ray
The Time over Threshold (ToT) parameter
X axis: time (s), y axis: signal amplitude (V)

## Slide 21
NEUTRON DETECTOR
Experimental data: obtaining on-surface FAST neutron flux
21

## Slide 22
Obtaining on-surface fast neutron flux
Placed Neutron detector in Lab B of the on-surface cleanroom
Took background data
Placed a Co60 gamma source on each segment of the detector and took data
Compared data
Estimated fast neutron flux
Seg1
Seg2
Seg3
Notes: pictures

## Slide 23
Gamma counts
Fast neutron counts
Thermal neutron counts
Seg1
Seg2
Seg3
Estimating on-surface neutron flux
Notes: Error bars

## Slide 24
Seg1
Seg2
Seg3
Co60
Estimating on-surface neutron flux
Notes: Error bars

## Slide 25
Seg1
Seg2
Seg3
Co60
Estimating on-surface neutron flux
Notes: Error bars

## Slide 26
Seg1
Seg2
Seg3
Co60
Estimating on-surface neutron flux
Notes: Error bars

## Slide 27
Estimating on-surface neutron flux

## Slide 28
Gamma counts
ON SURFACE NEUTRON FLUX: 11± 2 neutrons/cm²/day
neutron counts
Background flux and gamma flux merging
Estimating on-surface neutron flux
Comparing Co60 data to background data

## Slide 29
EXPACs Simulation
WHAT IS EXPACS?
EXcel-based Program for calculating Atmospheric Cosmic-ray Spectrum
It is based on the PARMA model: PHITS based Analytical Radiation Model in the Atmosphere
Comprises analytical functions with parameters fitted to reproduce the results of the extensive air shower simulations
ON SURFACE NEUTRON FLUX: 928 neutrons/cm2/day
Notes: Just show neutrons, muons instead of all of them

## Slide 30
NEUTRON DETECTOR
Obtain on surface Fast neutron flux
30

## Slide 31
Our experimental data VS EXPACs simulation
EXPACS simulation:
Fast neutron flux: 185 neutrons/cm2/day
DETECTOR data:
6 ± 2.0 fast neutrons/cm²/day
3.5 - 9 fast neutrons/cm²/day
Gamma counts
Thermal neutron counts
Fast neutron counts
cut obtained from literature
Data points
Notes: Make the numbers very big
title

## Slide 32
Our experimental data VS literature
Looked at previous experimental fast neutron data from MEASUREMENT OF THE FLUX AND ENERGY SPECTRUM OF COSMIC-INDUCED NEUTRONS ON THE GROUND
Integrated the spectrum
Used my intrinsic efficiency simulation to get fast neutron flux detected by detector
Detector Fast Neutron Flux (neutrons/cm2/day) | Literature’s Fast Neutron Flux (neutrons/cm2/day)
6 ± 2.0 fast neutrons | 2 -7

## Slide 33
Summary
Estimated neutron flux on surface
Estimated fast neutron flux on surface
Compared estimations with EXPACs and Literature
Notes: Cocnluding slide

## Slide 34: Next Steps
Do runs with 2 different gamma sources
Take detector underground
Calibrate detector with neutron sources
Obtain neutron flux underground
Notes: Prepare backup slide maybe for UG campaign

## Slide 39
Time over Threshold Parameter
Measures how long the signal amplitude stays above a certain offset (the “threshold”)
If the signal amplitude is tall and wide—possibly by a neutron
If it’s small and quick—possibly just noise or a gamma ray
Cuts can be set to determine the characteristic of the neutrons
The Time over Threshold (ToT) parameter
X axis: time (s), y axis: signal amplitude (V)

## Slide 40: HOW THE SIGNALS ARE DETECTED
SIGNAL CAPTURE
Each SiPM pair sends its signal to a discriminator
THRESHOLD CHECK
If signal > offset threshold  line is set to HIGH in Coincidence Unit
COINCIDENCE REQUIREMENT
If 2 lines are high within 30 ns, ToT counter starts
DECISION
If ToT within the cuts  likely a neutron  pulse produced
If not  not a neutron  no signal sent

## Slide 41
NEUTRON DETECTOR
GEANT4 SIMULATIONS OF OUR NEW DETECTOR
41

## Slide 42
42
LiF coating
He-4 gas
GEANT4 Simulation of Detector
x
y
z
Notes: Maybe show the axis or remove them

## Slide 43: GEANT4 SIMULATIONS OF DETECTOR: alpha and neutrons
1MeV Alpha particles
World Material: Vacuum
LiF cylinder
25meV neutrons
World Material: Vacuum
LiF cylinder
He-4 cylinder
1MeV Alpha particles
World Material: Vacuum
1 MeV neutrons
World Material: Vacuum
He-4 cylinder

## Slide 44
Testing Neutron Detector Simulation
Energy deposited by different neutron energies
Deposited Energy (MeV)
Events
Notes: Practice what I want to say more, remove the title

## Slide 45
Neutron and 𝜸-ray Discrimination by a Pressurized Helium-4 Based Scintillation Detector
Testing Neutron Detector Simulation
Energy deposited by different neutron energies
Deposited Energy (MeV)
Events
Notes: point out similarities in the both of them

## Slide 46
Testing Neutron Detector Efficiency
Fast neutron dose rate monitoring using off the shelf Helium-4 scintillation detectors
EXPERIMENT
Notes: Paper done previously
Tested the detector by sending neutrons of 3 different energies
See that the intrinicis efficiency decreased with neutron energy
So I did the same with my simulation- tested the efficiency

## Slide 47
Testing Neutron Detector Efficiency
Fast neutron dose rate monitoring using off the shelf Helium-4 scintillation detectors
SIMULATION
EXPERIMENT
Notes: This is the plot I have
You can see that when I sent same energies of neutrons, I got the exact same plot
This probably indicates that the neutron detector has very high efficiency, and the noise in the detector is very low. But we will need to do more analysis to confirm this.

## Slide 48: Cryogenic Underground TEst facility
Cleanroom
Ultra-pure water
Dry dilution fridge
48
Notes: The full form of CUTE is Cryogenic undergroudn testing facitily and it is located 2 kilometers underground at SNOLAB. But CUTE isn’t a detector itself. Instead, it’s a testing ground for experiments like dark matter and qubit characterizations.
CUTE consists of a clean room, a dilution fridge, a big tank of ultra pure water to shield components from neutron radiation
Because it’s so far underground, CUTE is shielded from cosmic radiation. And to test detectors that are supposed to catch very rare signals, we need to make sure the environment is as “quiet” as possible—no noise, no heat, and no shaking. CUTE uses a dilution refrigerator, clever trick with helium-3 and helium-4 gases to reach mind-blowing temperatures—down to 12 millikelvin, or about -273°C.
Formerly used for testing SuperCDMS dark matter detectors, CUTE now examines quantum chip performance in the absence of cosmic radiation.

## Slide 50
PREVIOUS NEUTRON MEASUREMENTS
50

## Slide 51
History of Measuring The Ambient Fast Neutron Flux
1. Found elements in norite rock and shotcrete
2. Use SOURCES4C and GEANT4
Notes: Estimated fast neutron flux: 4000 neutrons/m2/day (without experimental verification which is the problem)

## Slide 52
ISOTOPE | NORITE |  | SHOTCRETE | 
 | Concentration (ppm) | Neutron Flux (neutrons/year/cm3) | Concentration (ppm) | Neutron Flux (neutrons/year/cm3)
Total |  | 12.83 |  | 3.07
NORITE YIELD
SHOTCRETE YIELD
GEANT4: Estimated fast neutron flux of 4000 neutrons/m2/day
SOURCES4C Plots & Table
Notes: List where you got this information (maybe a source/name of paper)

## Slide 53
MY WORK
MY WORK TO OBTAIN THE ESTIMATED FAST NEUTRON SPECTRUM
53

## Slide 54
Tried to replicate their work
1. Obtain rock & shotcrete composition
2. Obtain U-238 and Th-232 decay chain information
Notes: Estimated fast neutron flux: 4000 neutrons/m2/day (without experimental verification which is the problem)

## Slide 55: New Theoretical Fast Neutron Spectrum from SOURCES4C
NORITE YIELD
SHOTCRETE YIELD
 | Old Data (Total neutrons/cm3/year) | My Data (Total neutrons/cm3/year)
Norite Yield | 12.83 | 12.97
Shotcrete Yield | 3.07 | 8.70
Notes: A lot of info on the slides
Remove the references
Speak about the process instead , put the title, then show the slides / break into 2 slides

## Slide 56
56
Arktis Discrimination Parameter
Arktis S670e Operation Manual
Notes: Counts as a function of the Time-over-Threshold discrimination parameter. The blue line is
the counts from an un-moderated Cf-252 source; the red one is the counts from a moderated Cf-252
source; and the green one is the pure gamma counts. The cuts to discriminate between the
gammas, fast and thermal neutrons are based on this spectrum.

## Slide 57
Fast neutron
He-4 nucleus in detector
How Arktis detects FAST neutrons
SiPM
Electronic board
The S-670e produces TTL pulses of different widths
57