## Slide 1
1

## Slide 2
Code is a tool to build simulations
MI beading workshop with Matt, Ty, and myself
2
  Photo credit: McDonald Institute

## Slide 3
CODE CRYOSTAT
TO
BUILDING A SINGLE-PHASE LIQUID ARGON CHAMBER
FROM
JULIA BRACHMAN (she/her)
SCALAR @ QUEEN’S UNIVERSITY
CASST 2026
3

## Slide 4
DO
HOW DO WE PHYSICS
with simulations?
1 Ar-39 beta decay
4
1 Am-241 alpha decay
Animation of our detector: scintillation photon tracks (blue) produced from…

## Slide 5
SINGLE-PHASE LAR CHAMBER
  Study technology for future liquid argon (LAr) detectors
Prototype
2-wall assembly
Photo credit to P. Taylor
5

## Slide 6
SCINTILLATION = flash of light when material absorbs energy
SINGLE-PHASE LAR CHAMBER
  Study technology for future liquid argon (LAr) detectors
    Ar-40 scintillates when particles interact
Nuclear recoils excite or ionize Ar-40, producing prompt scintillation light (S1) at 128nm.
6

## Slide 7
SINGLE-PHASE LAR CHAMBER
  Study technology for future liquid argon (LAr) detectors
    LAr scintillates when particles interact
    PEN shifts the
      light wavelength
    (128nm → 420nm)
7
Roll of PEN in our lab.
Photo credit Dr. Michela Lai.
Sheet of PEN (25 µm thick).

## Slide 8
SINGLE-PHASE LAR CHAMBER
  Study technology for future liquid argon (LAr) detectors
    LAr scintillates when particles interact
    PEN wavelength shifts light
    SiPMs observe light
8
Analog SiPM from our lab.
Photo credit Maxence Rault

## Slide 9
“CLEAN” CRYOGENIC ENVIRONMENT
  Backgrounds mitigated as much as possible
  Chamber to be operated at cryogenic temperatures (∼87 K)
  The SCALAR group has a cryostat locally
See another talk: H. Wen “Slow-Control Infrastructure for Noble Liquid Detector R&D”
9

## Slide 10
CONSTRUCTION
  Constructed of polytetrafluoroethylene (PTFE, Teflon)
  Initial prototype with high density polyethylene tested in liquid nitrogen
2-wall assembly after cryogenic test.
Photo credit to Peter Taylor
10

## Slide 11
CONSTRUCTION
  Constructed of polytetrafluoroethylene (PTFE, Teflon)
  Initial prototype tested
in liquid nitrogen
Final prototype will be octogonal chamber
11
PTFE geometry with SiPMs and PEN, as used in simulations.

## Slide 12
Full PEN WLS mode
COMPLEMENTING HARDWARE...
Strip PEN WLS mode
PEN on SiPMs WLS mode
  Placement of PEN WLS changes efficiency
  Optimized using simulation
12
WLS = wavelength shifter

## Slide 13
SIMULATION
Octogonal PFTE chamber filled with liquid argon using PEN wavelength shifter (WLS) and silicion photomultiplers (SiPMs) to detect scintillation from elastic scatters.
  UNDERSTAND YOUR DETECTOR
Open-source toolkit developed by CERN and used by (frustrated) physicists all over the world. C++ and object-oriented, it allows users to track particle paths using Monte-Carlo methods in user-defined geometries.
  DOWNLOAD GEANT4
...
  BUILD YOUR SIMULATION
13

## Slide 14
How can we predict what happens when radiation interacts with our detector?
14

## Slide 15
Build a digital model of the single-phase chamber
How can we predict what happens when radiation interacts with our detector?
15

## Slide 16
Build a digital model of the single-phase chamber
Define detector materials and geometry
How can we predict what happens when radiation interacts with our detector?
16

## Slide 17
Build a digital model of the single-phase chamber
Define detector materials and geometry
LAr
PTFE
SiPMs
WLS
How can we predict what happens when radiation interacts with our detector?
CAD model
Geant4 model
17
Cryostat

## Slide 18
Build a digital model of the single-phase chamber
Define detector materials and geometry
Define radioactive sources
LAr
PTFE
SiPMs
WLS
How can we predict what happens when radiation interacts with our detector?
18
Cryostat

## Slide 19
Build a digital model of the single-phase chamber
Define detector materials and geometry
Define radioactive sources
Ar-39
K-40
Alphas
Position
Energy
LAr
PTFE
Cryostat
SiPMs
WLS
How can we predict what happens when radiation interacts with our detector?
19

## Slide 20
Define radioactive sources e.g.
Ar-39
Distributed through bulk volume
Position
Energy
Density | 1.396 g/cm³ at 84K
Optical properties | Refractive index, Rayleigh scattering length, optical range 2.0–10.6 eV (620–117 nm)
Scintillation yield | 40 photons/keV
Absorption length | 20m
20

## Slide 21
Build a digital model of the single-phase chamber
How can we predict what happens when radiation interacts with our detector?
Select physical processes
21

## Slide 22
Build a digital model of the single-phase chamber
How can we predict what happens when radiation interacts with our detector?
Select physical processes
Electromagnetic interactions
Optical photons
Scintillation
Absorption
WLS
22

## Slide 23
Build a digital model of the single-phase chamber
How can we predict what happens when radiation interacts with our detector?
Select physical processes
Generate Monte Carlo events
Sample particle type
Sample energy
Sample location
23

## Slide 24
Build a digital model of the single-phase chamber
How can we predict what happens when radiation interacts with our detector?
Select physical processes
Generate Monte Carlo events
Track every particle through the detector
and simulate all interactions
24

## Slide 25
Generate events e.g.
Ar-39
Electron deposits energy in LAr, producing scintillation (VUV) photons.
Visualizer shows 4 particle tracks from 1 event.
25

## Slide 26
Build a digital model of the single-phase chamber
How can we predict what happens when radiation interacts with our detector?
Select physical processes
Generate Monte Carlo events
Track every particle through the detector
and simulate all interactions
Record detector observables
Energy deposited
Photons produced
SiPM hits
26

## Slide 27
Build a digital model of the single-phase chamber
How can we predict what happens when radiation interacts with our detector?
Select physical processes
Generate Monte Carlo events
Track every particle through the detector
and simulate all interactions
Record detector observables
Analyze and validate results
Spectra
Light yield
Efficiencies
Backgrounds
27

## Slide 28
Results e.g. Amount of scintillation produced
Ar-39
28
  Excited molecular states of Ar (“excimers”) release light when they decay
  Deposited energy in LAr vs amount of light produced is linear
Yield = 39.999±0.025 photons/keV
Slope = Scintillation yield

## Slide 29
29
  Quenching : processes that divert deposited energy away from scintillation, e.g. into heat, reducing the detectable light yield.
  Alphas experience strong quenching
  Scintillation yield is reduced to
  70% of full yield
  Matches theoretical Q value (~0.7)
Yield: 28.708±0.0174 photons/keV
Results e.g. Amount of scintillation produced
Alpha gun

## Slide 30
104 photon tracks
from 1 alpha-gun event
4 photon tracks
from 1 Ar-39 event
30

## Slide 31
THANK YOU
Scan to connect with me on Linkedin!
Julia Brachman
22gn16@queensu.ca
Queen’s University
31

## Slide 32
BACKUP SLIDES
32

## Slide 33
DIRECT DETECTION WITH LIQUID ARGON
EXTRA SLIDES
  Nuclear recoils excite or ionize Ar-40, producing prompt scintillation light (S1, 128nm).
  Non-recombined ionization electrons can produce secondary scintillation (S2) through electroluminescence.
Single-phase chambers only collect S1
Dual-phase chambers can collect S1 & S2
33

## Slide 34
DUAL-PHASE (TPC) CHAMBERS
EXTRA SLIDES
  “Time projection chambers”
  Drift ionization electrons are directed from a liquid to a gaseous layer
  Requires complex high-voltage and fine-tuned electric fields within a cryogenic system
Figure from “Direct Dark Matter Detection with Darkside-20k experiment” [slides], by Manthos, I., 2022, University of Birmingham
34

## Slide 35
COMPONENTS OF THE GEANT4 CODE
EXTRA SLIDES
  Macros are plain text files with built-in user interface (UI) commands
  Used to customize simulation runs, called with the executable
Example screenshot from a macro
35

## Slide 36
HOW DO WE VALIDATE BACKGROUND GENERATOR?
EXTRA SLIDES
  Compare sampled energy to expectation
K-40 beta sampled energy spectrum
Ar-39 beta sampled energy spectrum
36

## Slide 37
HOW DO WE VALIDATE BACKGROUND GENERATOR?
EXTRA SLIDES
  Compare sampled position to expectation
K-40 EC gamma sampled position
Ar-39 beta sampled position
37

## Slide 38
  Determined from active volume, density, and specific activity
  Specific activity is taken from literature
  Volume is determined by our detector
HOW DO WE PREDICT ACTIVITY?
EXTRA SLIDES
38

## Slide 39
SCINTILLATION YIELD
EXTRA SLIDES
39
Excited Ar (“excimers”) release light when they decay
  Scintillation: The flash of light after a material absorbs energy
  Yield depends on type of radiation and dE/dx
    Higher ionization density increases non-radiative recombination, thus reducing light yield
  Quenching: any process that reduces interupts the excimer from producing VUV scintillation

## Slide 40
TYPES OF SIGNALS IN LIQUID ARGON
EXTRA SLIDES
40
Electron recoil
Energy deposited by electrons.
Relatively low ionization density.
E.g. betas from
Ar-39 → K-39 decay
Nuclear recoil
Energy deposited by recoiling argon nucleus.
E.g. WIMP signal on Ar-40
Alpha events
Energy deposited by alphas.
More densely ionizing tracks.
E.g. Rn-222, Po-210 decay chains

## Slide 41
TYPES OF SIGNALS IN LIQUID ARGON
EXTRA SLIDES
41
Electron recoil
Energy deposited by electrons.
Relatively low ionization density.
E.g. betas from
Ar-39 → K-39 decay
Nuclear recoil
Energy deposited by recoiling argon nucleus.
E.g. WIMP signal on Ar-40
Alpha events
Energy deposited by alphas.
More densely ionizing tracks.
E.g. Rn-222, Po-210 decay chains
More quenching!

## Slide 42
ALPHA QUENCHING
EXTRA SLIDES
42
Adhikari, P et al. DEAP Collaboration. (2025). Relative measurement and extrapolation of the scintillation quenching factor of alpha-particles in liquid argon using DEAP-3600 data. Eur. Phys. J. C, 85, 87. 10.1140/epjc/s10052-024-13518-7 / arXiv:2406.1859
  DEAP-3600 calculated the quenching factor of alpha particles as function of energy
  For 1 Mev, Q ~ 0.7

## Slide 43
What is PEN?
EXTRA SLIDES
43
  Polyethylene naphthalate
  Industrial-grade thermoplastic polyester
  Solid thin sheets (~25 µm)
  Absorbs vacuum ultraviolet (VUV) scintillation light and re-emits it as visible blue light
  Boosts photosensor efficiency
  Another common wavelength-shifter is TPB, which is evaporated on surfaces instead of being a sheet.