## Slide 1
Servers and Simulations:
Building Critical Infrastructure for the NEWS-G Experiment
Time
Andrew Gault
Summer Student Researcher
Queen’s University, NEWS-G

## Slide 2: Simulations
Initial goal: Replicate our current NEWS-G sphere setup given a 3D modeling software, CADQuery, that uses programming to make objects, and COMSOL Multiphysics to setup the electrostatics and run simulations to answer questions like what is the best 19-anode sensor design.
2

## Slide 3: CADQuery -- Start
Software that uses Python code to procedurally create 3D objects.
I then automated customizing three different designs.
Used a printed model I found of an 11 Anode Tetrahedral Achinos sensor as reference to recreate in the software.
3

## Slide 4: CADQuery -- Tetrahedral
WHAT?
Evenly spaced rows filled with nodes with one node on the bottom. Each row is offset to make a triangular configuration.
HOW?
Uses a set of polar arrays, one for the rows and one for each node within their respective rows.
Automatically determines how many nodes to put on each row based on the number of nodes and rows requested.
CONFIG?
Number of rows and total number of nodes can be customized.
4

## Slide 5: CADQuery -- Canonical Fibonacci Lattice
WHAT?
A modified Fibonacci Lattice to improve packing (maximize the minimum distance between any two neighbouring nodes).
HOW?
Uses the following formulas to calculate the angles:
Uses quaternions and the vector V1 × V2 | V1 = origin to node and V2 = origin to -Z pole to rotate all nodes so there is one at the -Z pole when the config does not already put one there.
CONFIG?
Number of nodes, force bottom node (True/False).
5

## Slide 6: CADQuery -- Regular Dodecahedron
WHAT?
Largest platonic solid (identical faces with equal-length edges) in terms of vertices. Not as well packed as canonical lattice, but due to the uniform spread, likely to be better for us.
HOW?
Manually inputted x, y, z coordinates for each node position as it is a unique polyhedron.
6
Notes: Much quicker and simpler to manually set each node position.

## Slide 7: CADQuery -- Config
Contains easy-to-modify parameters at the top to quickly tweak previous designs.
If a person wants to make an entirely new design, objects like the node and useful code are held within utility functions and, along with the rest of the code, are well documented.
Tetrahedral:
19 anodes 4 rows
19 anodes 3 rows
25 anodes 5 rows
Canonical Lattice:
36 anodes
90 anodes
Regular Dodecahedron:
19 anodes
Time
7

## Slide 8: COMSOL Multiphysics
Umbrella
Glass
Anodes
Copper Pipe
Detector /Sphere
8

## Slide 9: COMSOL Multiphysics
Designed a single COMSOL file that contains all the infrastructure needed to switch between and build off of sensor types imported from CADQuery.
Various other easily modifiable parameters to change the sensor and detector as a whole.
9

## Slide 10: COMSOL Multiphysics Final 19-anode sensor designs
4 Row Tetrahedral
Canonical Fibonacci Lattice
Regular Dodecahedron
10
Notes: Test for uniformity. Looking for high, even gain/number of electrons per anode.

## Slide 11: COMSOL Multiphysics
I completely refurbished the dedicated COMSOL computer with a new SSD, put the hard drive array into RAID 10 (faster with data loss redundancy), and a fresh install of all necessary software with several other optimizations implemented.
11

## Slide 12: COMSOL Multiphysics
Ran a batch simulation to find where the electric field’s Enorm in a multi-anode sensor looks like a single anode sensor. Has 120 combinations of parameters.
Wrote a program to analyze the data. Finds distance from center that Enorm ~ A/r2 where A is a real number. Found at R2 of 0.9, 0.95, 0.98, and 0.99. By comparing the calculated distances given each parameter combination a law can be formed to give us an approximate answer.
12
Notes: With a new PC set up I was able to run a batch simulation over 120 parametric combinations to try and find the distance from the center of the detector where a multi-anode looks like a single anode in terms of its electric field. The simulations finished successfully and I wrote a program to help the next person analyze the data and come to a useful conclusion.

## Slide 13: Servers
13

## Slide 14: Background
What was
Used HTTP (all network traffic visible to malicious actors.)
Comments not functional.
Plots open in new tabs one at a time.
Rigid headers (what you see is what you get.)
No filtering or searching (aside from using CTRL-F to search for terms that are loaded in the page.)
Can only view one sphere’s runs at a time.
Etc.
14

## Slide 15: Background
Comparison
Time
New design:
Old design:
15

## Slide 16: Structure New design
Docker - Lets groups of functions run inside containers, which are separate simplified virtual machines for enhanced security and faster updates.
Front-end (what the user sees/the website)
Back-end
Database (Holds run data)
(Abstracted interface
between front-end and database)
16

## Slide 17: Structure
Front-end (what the user sees/the website)
Back-end
Database (Holds run data)
(Abstracted interface
between front-end and database)
Uses JSON files for each data point/run. Allows for different fields in future if they change.
Enables fast routing and prevents malicious injection into the database.
Time
React
Vite
Bundles, optimizes, and quickly builds/deploys javascript and css files.
To create interactive websites that load and change elements without the page reloading/changing.
NGINX (Engine X)
Exposes website to internet and manages
web traffic (sending and receiving data.)
17

## Slide 18: End Result
Login Page for basic security:
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
Time
18
Notes: Login to Sphere 2 Database before presenting to avoid giving out username and password.

## Slide 19: End Result
Live Demo!
19

## Slide 20: Thank you!
Questions?
20

## Slide 21: Extra Slides
21

## Slide 22: CADQuery -- Diagram/Legend
Node
Extrusion
Sensor Head/Umbrella
Wire
Anode
22
Notes: For context